DV701

5.8GHz Diversity LCD Screen Receiver Monitor

- 屏幕尺寸：7”

- 屏幕类型：TFT LCD Screen/long life, LED backlight

- 分辨率： 800*480

- 亮度： 450cd/m2

- 可视角度：140/120度 (水平/垂直)

- * 存储器：内存 SD(TF)卡最大支持32GB
* 无线接收： 5.8G 32频道，-90dBm接收灵敏度
* 菜单语言：5种
* AV输出：单声道、视频输出
* AV输入：单声道、视频输入
* 直流输入：7-28V
* DATA OUT接口：3.5mm插头
* USB通信：USB2.0

- 屏幕尺寸：7”

- 屏幕类型：TFT LCD Screen/long life, LED backlight

- 分辨率： 800*480

- 亮度： 450cd/m2

- 可视角度：140/120度 (水平/垂直)

- * 存储器：内存 SD(TF)卡最大支持32GB
* 无线接收： 5.8G 32频道，-90dBm接收灵敏度
* 菜单语言：5种
* AV输出：单声道、视频输出
* AV输入：单声道、视频输入
* 直流输入：7-28V
* DATA OUT接口：3.5mm插头
* USB通信：USB2.0

Ⅰ.Features：

- Built in 5.8 GHz wireless receiving signal and input signal from outside

- 4 Frequency Bands and total 32 Channels, compatible with most of the 5.8G wireless equipment

- Diversity wireless receives output, can choose and receive the stronger signal automatically

- Can receiver two different channels of RF signals simultaneous

- Built-in 2CH 5.8Ghz AV output and 1CH AV input

- Built-in 2500mAh high volume Li-Polymer battery，easy to carry for outdoor using

- A key to automatic signal search，simple operation

- Work status OSD display: Always be aware of the device working condition

Ⅱ．Specification:

- Wireless receiver: 5.8G/32 Channels

- Receiving sensitivity: -90dBm

- Screen size：7”

- Screen type：TFT LCD Screen/long life, LED backlight

- Resolution： 800*480

- Brightness： 450cd/m2

- View Angle：140/120degree (Horizontal/Vertical)

- Memory-storing approach：Memory SD (TF) card，the maximum support is 32GB

- Language：5 kinds

- Input/Output：AV signal， single track

- Built-in Li-po battery： 2500mAH/7.4V

- OSD display: RSSI indication; Battery volume indicator; RF working Channel indication

- Input power：DC current 7-28V (3s/4s/5s/6s)

- Charging currency： 850mA @12V ( Maximum )

- Power Consumption： 650 mA @12V（maximum）

- Working temperature ： -10℃~ + 65 ℃

- signal output interface：2.5mm plug

- communication interface：USB2.0

- Size 菜单语言菜size si：180 x 124 x 25mm  Note ( Sunshield height: 106mm)

Band and Channel selection:

| Ch | CH 1 | CH 2 | CH 3 | CH 4 | CH 5 | CH 6 | CH 7 | CH 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Brand |  |  |  |  |  |  |  |  |
| A | 5865 MHZ | 5845 MHZ | 5825 MHZ | 5805 MHZ | 5785 MHZ | 5765 MHZ | 5745 MHZ | 5725 MHZ |
| B | 5733 MHZ | 5752 MHZ | 5771 MHZ | 5790 MHZ | 5809 MHZ | 5828 MHZ | 5847 MHZ | 5866 MHZ |
| E | 5705 MHZ | 5685 MHZ | 5665 MHZ | 5645 MHZ | 5885 MHZ | 5905 MHZ | 5925 MHZ | 5945 MHZ |
| F | 5740 MHZ | 5760 MHZ | 5780 MHZ | 5800 MHZ | 5820 MHZ | 5840 MHZ | 5860 MHZ | 5880 MHZ |

### Ⅲ.The appearance of the product structure diagram:

### Front view

### 2) Back view

Ⅳ.Key and interface operation introduction

When there is no signal on the screen, please press any key for one time at first, when it showing

The indicator, then the key starts to work.

[ 1 ] KEY:  press short time for 0.5 seconds, long press for 2 seconds

● REC/PLAY/OK：

1. One short press start to record, the recording lasts for 10 minutes it will be a section automatically, one short presses again then it withdrawing from record.

2. Long press starts to Replay Mode, press “GROUP/+”or” CHANNEL/-”,choosing the replay mode time, short presses “REC/PLAY/OK” again it starts to replay, one long presses again then it withdrawing from Replay mode.

3. When press the “MENU”, it starts the menu mode, press OK key for confirm.

● SEARCH/SOURCE：

1. Press this button to enter the signal search, it will automatically search for the signals to a certain strength signal and stops on that channel , if the signal is not found, it will stop on the channel before starting the search;

Note: During the searching process, press any key will not work.

Long press changes the signal source:

DIVERSITY： True diversity reception mode，it will show the stronger signal between Ra A and RF B to get the better reception；Corresponding to the RF- A and RF- B indicator LED will flash alternately.

RF A：RF A single received signal

RF B：RF B single received signal

AV IN：AV signal from external；

- MENU：

1. Short press enter menu choosing Mode, press “GROUP/+”or “CHANNEL/-”,choose program setting, press “REC/PLAY/OK” and choose set up program, then enter into sub-menu, press the “GROUP/+”or “CHANNEL/-” again and set up the parameter, press the “REC/PLAY/OK ”to confirm.

Note: After setting the time and date, please choose the make of “√”and press “REC/PLAY/OK”to confirm, then the time and date works.

● GROUP/+：

1. Short press the GROUP, A-B-E-F four bands cycle selection

2. Long press for audio increasing;

3. MENU pressed, this button is used as UP↑

●CHANNEL/-：

1. Short press CH, 1-8 channels cycles

2. Long press for audio decreasing;

3 .MENU pressed, this button is used as Down ↓

● POWER：

1. Press 3s for opening, press 0.5s for shutdown.

[ 2 ] JACK:

● RF A AV OUT：RF A receives the output of an AV signal，RF A mode must.

● RF B AV OUT：RF B receives the output of a n AV signal ，RF B mode must.

● DC/+12V：DC IN, +12V power supply , operating current of the device is 650mA @ 12V, built-in battery maximum charge current is 800mA @ 12V; if the device is working when charging , please pay attention to select the charging equipment which the rated current is 2A/12V-28.

● SD card jack: please make sure the SD card insert in the right direction (please buy the regular brand SD card)

Ⅴ.Battery instruction：

Built-in 7.4V/ 2500mAH high-capacity Li- polymer battery, when the battery is charging，the red LED will light(there is a cell indictor on the bottom left of the device)when charging is completed，the red Led will turn off.

Note: If the device is not used for a long time, please charge once every 3-6 months to protect the battery.

Ⅵ.Package Included:

- LCD Recevier            * 1

- Antennas                * 2

- AV Cables               * 2

- Power Cable             * 1

- USB cable                *1

- 12/2A charger            * 1

- English/Chinese manual    *1