MC91系列MINI CCTV

使用说明书INSTRUCTION

MC91 MINI CCTV CAMERA

一、概述

感谢您使用我们的产品,在使用产品前,请仔细阅读使用说明书,以确保正确使用此系列产品。使用说明书应妥善保存,以备后用。

摄像机采用高灵敏度CMOS成像器件，具有卓越的影像功能和极低的照度。整机稳定性强,具有极长的工作寿命.该系列产品体积比手指还小，最小重量5克，安装简便，适合隐蔽式监控。

二、主要特性

- 尺寸小易于安装在微小的空间和细小的管道中；

- 配备可拆安装支架可方便地将摄像头固定在墙面上，另还配可拆底盘平放于任何桌面；

- 支架可360度旋转，全方位监控；

- 高解析度、高灵敏度和高信噪比；

- 白天夜晚双模式自动切换；

- 低照度、低功耗；

- 第4代CMOS传感器+DSP数字芯片合成技术、图像清晰不失真。

三、注意事项

- 轻拿轻放

- 请不要把摄像机置于潮湿或被雨淋的地方，或在潮湿的地方操作，一旦摄像机湿了，请立即关掉电源，找专业人员维修。

- 请不要把摄像机对着太阳光，不要在聚光灯或别的强光、反光旁边工作使用。

- 请在规定的温度、湿度和电源范围内操作摄像机

四、产品外观及型号

MC91                  MC91A                  MC91B18

MC91AB18             MC91P36                MC91AP36

五、产品结构尺寸

MC91结构尺寸                    MC91A结构尺寸

MC91B18结构尺寸                MC91AB18结构尺寸

五、产品结构尺寸

MC91P36结构尺寸                 MC91AP36结构尺寸

六、MC91摄像机模块产品规格

| 摄像器件 | 1/4 CMOS图像传感器 |
| --- | --- |
| 系统制式 | NTSC | PAL |
| 影像总像素 | NTSC：720（H）×480（V） | PAL：720（H）×576（V） |
| 图像传感器尺寸 | 3.584mm（H）×2.688mm（V） |
| 水平清晰度 | 480TV Lines |
| 最低照度 | 0.05Lux/F1.2 |
| 镜头 & 视角 | F1.2 / 90 ° |
| 信噪比 | 大于48dB |
| 功 能 | 自动增益控制 | OUT |
|  | 白平衡控制 | OUT |
|  | 背光补偿 | OUT |
| 视频输出 | 1.0V p-p/75欧姆 |
| 音频输出 | 1.0V p-p/1K欧姆 |
| 净重（克） | 5克 MC91A：5克 |
| 尺寸(长X宽X高) | MC91：15.5X15.5x20mm; MC91A: 15.5X15.5x22.5mm |
| 电流 | DC12V: 45mA DC5V: 95mA DC12V: 35mA |
| 电 源 | DC:3.6V-24V （3.6-24V ） |
| 环境温度 | - 20°C ~ + 50°C ，相对湿度85﹪ |
| 线材接线： | PIN1(红色接DC5V/DC12 PIN2(黑色接GND PIN3(黄色接VIDEO OUT PIN4(白色接AUDIO OUT |

六、MC91B18摄像机模块产品规格

| 摄像器件 | 1/4 CMOS图像传感器 |
| --- | --- |
| 系统制式 | NTSC | PAL |
| 影像总像素 | NTSC：720（H）×480（V） | PAL：720（H）×576（V） |
| 图像传感器尺寸 | 3.584mm（H）×2.688mm（V） |
| 水平清晰度 | 480TV Lines |
| 最低照度 | 0.1Lux/F2.8 |
| 镜头 & 视角 | F2.8 / 170 ° |
| 信噪比 | 大于48dB |
| 功 能 | 自动增益控制 | OUT |
|  | 白平衡控制 | OUT |
|  | 背光补偿 | OUT |
| 视频输出 | 1.0V p-p/75欧姆 |
| 音频输出 | 1.0V p-p/1K欧姆 |
| 净重（克） | 8克 MC91A：5克 |
| 尺寸(长X宽X高) | MC91B18：15.5X15.5x23mm; MC91AB18: 15.5X15.5x26mm |
| 电流 | DC12V: 45mA DC5V: 95mA DC12V: 35mA |
| 电 源 | DC:3.6V-24V （3.6-24V ） |
| 环境温度 | - 20°C ~ + 50°C ，相对湿度85﹪ |
| 线材接线： | PIN1(红色接DC5V/DC12 PIN2(黑色接GND PIN3(黄色接VIDEO OUT PIN4(白色接AUDIO OUT |

六、MC91P36摄像机模块产品规格

| 摄像器件 | 1/4 CMOS图像传感器 |
| --- | --- |
| 系统制式 | NTSC | PAL |
| 影像总像素 | NTSC：720（H）×480（V） | PAL：720（H）×576（V） |
| 图像传感器尺寸 | 3.584mm（H）×2.688mm（V） |
| 水平清晰度 | 480TV Lines |
| 最低照度 | 0.1Lux/F2.8 |
| 镜头 & 视角 | F2.8 / 90 ° |
| 信噪比 | 大于48dB |
| 功 能 | 自动增益控制 | OUT |
|  | 白平衡控制 | OUT |
|  | 背光补偿 | OUT |
| 视频输出 | 1.0V p-p/75欧姆 |
| 音频输出 | 1.0V p-p/1K欧姆 |
| 净重（克） | 6克 MC91A：5克 |
| 尺寸(长X宽X高) | MC91B18：15.5X15.5x20mm; MC91AB18: 15.5X15.5x22.5mm |
| 电流 | DC12V: 45mA DC5V: 95mA DC12V: 35mA |
| 电 源 | DC:3.6V-24V （3.6-24V ） |
| 环境温度 | - 20°C ~ + 50°C ，相对湿度85﹪ |
| 线材接线： | PIN1(红色接DC5V/DC12 PIN2(黑色接GND PIN3(黄色接VIDEO OUT PIN4(白色接AUDIO OUT |

I. Introduction

Thank you for choosing our products. Before using, please read the instruction carefully to assure good performance. This manual should be kept well in case any necessary reference in future.

These cameras come with high sensitive CMOS sensor, which has excellent video function and very low illumination. They are of high stability and ultra long working life.  Their sizes are as small as coin. Weight is 5g only. It’s very suitable for hidden surveillance.

II. Main Features

- Small Size: easy to install into narrow room and slim tube, etc.;

- Easy Installation: Simply place it at any desktop with its detachable base station, or screw it on the wall with the detachable stand;

- Camera stand can rotate 360 degrees, all-round monitoring

- High resolution, high sensitivity, high SNR;

- Day & night dual mode auto switch;

- Low Illumination, Low Current and power consumption;

- CMOS sensor generation IV+DSP chip offer true color & HD video.

III. Notice

1. Handle with care.

2. Please don’t place or operate camera in damp places or with rain. Once camera is wet, please shut off the power immediately and contact professional persons to repair.

3. Please don’t face camera to sunlight. Don’t operate it over the spotlight or other strong light, reflector.

4. Please operate cameras under the stated temperature, humidity and power supply.

IV. Image and Model No.

MC91                  MC91A                  MC91B18

MC91AB18             MC91P36                  MC91AP36

V. Outline Size

MC91 Outline Size                     MC91A Outline Size

MC91B18 Outline Size               MC91AB18 Outline Size

V. Outline Size

MC91P36 Outline Size              MC91AP36 Outline Size

VI. MC91 Specification

| PICK UP ELEMENT | Single chip 1/4CMOS |
| --- | --- |
| SYSTEM | NTSC | PAL |
| NUMBER OF PIXEL | NTSC：720（H）×480（V） | PAL：720（H）×576（V） |
| SENSOR DIMENSION | 3.584mm（H）×2.688mm（V） |
| HORIZONTAL RESOLUTION | Approximately 480TV Lines |
| SENSITIVITY | 0.05Lux/F1.2 |
| LENS & VIEW ANGLE | F1.2 / 90° |
| S/N RATIO | 48dB |
| AUTO GAIN CONTROL | OUT |
| WHITE BALANCE CONTROL | OUT |
| BACK LIGHT COMPENSATION | OUT |
| VIDEO OUT | 1.0V p-p/75ohm |
| AUDIO OUT | 1.0V p-p/1Kohm |
| WEIGHT | 5g MC900D-V9：3-5克 |
| SIZE（LXWXH） | MC91：15.5X15.5X20mm; MC91A: 15.5X15.5X22.5mm |
| WORK CURRENT | DC12V: 45mA DC5V: 95mA DC12V: 35mA |
| POWER REQUIREMENT | DC:3.6V-24V DC12V:（5-16V ） |
| OPERATING TEMPERATURE | - 10° C ~ +50°C ，less than 90% RH |
| Connection | PIN1( Red DC5V /12V PIN2( Black GND PIN3( Yellow VIDEO OUT PIN4( White AUDIO OUT |

VI. MC91B18 Specification

| PICK UP ELEMENT | Single chip 1/4CMOS |
| --- | --- |
| SYSTEM | NTSC | PAL |
| NUMBER OF PIXEL | NTSC：720（H）×480（V） | PAL：720（H）×576（V） |
| SENSOR DIMENSION | 3.584mm（H）×2.688mm（V） |
| HORIZONTAL RESOLUTION | Approximately 480TV Lines |
| SENSITIVITY | 0.1Lux/F2.8 |
| LENS & VIEW ANGLE | F2.8 / 170° |
| S/N RATIO | 48dB |
| AUTO GAIN CONTROL | OUT |
| WHITE BALANCE CONTROL | OUT |
| BACK LIGHT COMPENSATION | OUT |
| VIDEO OUT | 1.0V p-p/75ohm |
| AUDIO OUT | 1.0V p-p/1Kohm |
| WEIGHT | 8g MC900D-V9：3-5克 |
| SIZE(LXWXH) | MC91B18：15.5X15.5X23mm; MC91AB18: 15.5X15.5X26mm |
| WORK CURRENT | DC12V: 45mA DC5V: 95mA DC12V: 35mA |
| POWER REQUIREMENT | DC:3.6V-24V DC12V:（5-16V ） |
| OPERATING TEMPERATURE | - 10° C ~ +50°C ，less than 90% RH |
| Connection | PIN1( Red DC5V /12V PIN2( Black GND PIN3( Yellow VIDEO OUT PIN4( White AUDIO OUT |

VI. MC91P36 Specification

| PICK UP ELEMENT | Single chip 1/4CMOS |
| --- | --- |
| SYSTEM | NTSC | PAL |
| NUMBER OF PIXEL | NTSC：720（H）×480（V） | PAL：720（H）×576（V） |
| SENSOR DIMENSION | 3.584mm（H）×2.688mm（V） |
| HORIZONTAL RESOLUTION | Approximately 480TV Lines |
| SENSITIVITY | 0.1Lux/F2.8 |
| LENS & VIEW ANGLE | F2.8 / 90° |
| S/N RATIO | 48dB |
| AUTO GAIN CONTROL | OUT |
| WHITE BALANCE CONTROL | OUT |
| BACK LIGHT COMPENSATION | OUT |
| VIDEO OUT | 1.0V p-p/75ohm |
| AUDIO OUT | 1.0V p-p/1Kohm |
| WEIGHT | 6g MC900D-V9：3-5克 |
| SIZE(LXWXH) | MC91P36：15.5X15.5X20mm; MC91AP36: 15.5X15.5X22.5mm |
| WORK CURRENT | DC12V: 45mA DC5V: 95mA DC12V: 35mA |
| POWER REQUIREMENT | DC:3.6V-24V DC12V:（5-16V ） |
| OPERATING TEMPERATURE | - 10° C ~ +50°C ，less than 90% RH |
| Connection | PIN1( Red DC5V /12V PIN2( Black GND PIN3( Yellow VIDEO OUT PIN4( White AUDIO OUT |