AIO HD 1080P FPV Wireless Transmitter DV Camera

SKY-HD01

Features:

- Full HD 1080p 30fps

- Built-in 4 Bands 32CH 5.8Ghz 400mw transmitter

- LENS Rotation range: ±45 degrees

- FOV angel: 150 degrees (Diagonal)

- Support PWM remote control

- Support OSD

Function Diagram

Precautions

- Please make sure the DV battery is full recharged before use

- Please connect the Micro 5Pin USB cable to the DV and the other end to the 5V power source( Power adapter, PC or power-bank

- It’ll take about 90mins to recharge. Charge Led is in red while charging and in green after fully charged.

- Please make sure power source is no less than 5V/1.2A while recharging and recording at the same time.

- The PWM remote control feature fulfill with a 3 Switch of the remote controller.

- The PWM remote control feature fulfill with suited LCD display products.

Power Key/Led

- Long press Power button for 3 seconds to turn on the PWM remote Control and blue led flashes. Short press again to turn on the camera and in camera review mode.(Blue Led off after turning on and Red constant light)

- Short press once to enter system menu under Review mode

- It’s ESC button in menu mode

- Long press 3 seconds to turn off the device.

Photo Key

- Short press once to capture a photo in review mode

- Short press once to capture a photo in recording mode

Record Key

- Short press once to start recording in review mode and press to stop recording

- Long press 3 second in review mode to enter playback mode

- It’s OK button in menu mode

UP key

- Short press once to setup the Bands

- It’s UP button in menu mode

Down Key

- Short press once to setup the channels

- It’s Down button in menu mode

Record Mode

- Red LED flashes while recording and REC icon in red

- Video files will be auto saved (reach setup video length)and create a new file to continue recording.(recording time will be displayed on the screen until stop recording)

- It’s OK to capture photo while recording

Playback Mode

- Features of the buttons:

: Play/Pause

: Stop/Menu/Esc

: UP

: Down

Remote Bands/Channels Setup

- Connect 3P remote control cable to one of PWM Channel of the receiver and other end to the S1 port on the camera

- To assign a Channel to Bands/Channels Setup and assign another 3 switch, C-H for Bands, C-L for channels

Remote camera control ( fulfill with suited LCD display products)

- Connect 3P remote control cable to one of PWM channels of the receiver and the other end to the S2 port of the camera

- To assign a channel to camera remote control port S2

- Connect the LCD monitor remote control output port to the PWM input of the remote control. Then you can operate the camera via the LCD monitor

External OSD Device

- Press both UP/DOWN button at the same time in review mode to switch the camera to OSD transmitter mode. Then the video output to the external OSD and then back to the camera

- Press the two buttons again back to normal video transmitter mode

Menu List

| Video Size | 1080p30(default)/720p60/720p3 |
| --- | --- |
| Video quality | High(default)/Medium/Low |
| Video Length | 30Min.(default)/20Min./10Min./Min. |
| Auto REC | On(default)/Off |
| Time Stamp | Off(default)/Date Only/Date&Time |
| Audio Record | On(default)/Off |
| EV | +0.0 |
| Orientation | Normal(default)/180 |
| OSD | On(default)/Off |
| Setup | Language | English(default)/Simplified Chinese/Traditional Chinese/French/Germany/Italian/Spanish/Portuguese/Japanese |
|  | Date Input | 2015 / 08 / 10 |
|  | Time Input | 10:35:00 |
|  | Date Format | YY/MM/DD MM/DD/YY DD/MM/YY |
|  | Format |  |
|  | Auto shutdown | Off(Default)/5Min/10Min/15Min/20Min/30Min |
|  | Light Freq. | 60Hz(default)/50Hz |
|  | TV Output | NTSC(Default)/PAL |
|  | USB | DC IN(Default)/Disk Drive |
|  | Sys. Reset |  |
|  | FW Upgrade |  |
|  | FW Version | 2015.03.10.01 |

Specifications

| Camera | FOV | 150 degrees (Diagonal) |
| --- | --- | --- |
|  | LENS Rotation range | ±45 degrees |
|  | Resolution | 1920x1080p30,1280x720p60, 1280x720p30 |
|  | Micro SD | Support to 32GB |
|  | Video Compression | h.264 |
|  | Picture | JPEG |
|  | Record quality | High,Mid,Low |
|  | Microphone | Digital |
| Wireless Transmitter | ISM 5.8GHz 32 Channel, Transmitter. |
|  | Frequency | Band | CH 1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 |
|  |  | A | 5865M | 5845M | 5825M | 5805M | 5785M | 5765M | 5745M | 5725M |
|  |  | B | 5733M | 5752M | 5771M | 5790M | 5809M | 5828M | 5847M | 5866M |
|  |  | E | 5705M | 5685M | 5665M | 5645M | 5885M | 5905M | 5925M | 5945M |
|  |  | F | 5740M | 5760M | 5780M | 5800M | 5820M | 5840M | 5860M | 5880M |
|  | RF Output Power | 24dBm±1dBm |
|  | RF Output Impedance | 50ohm, SMA port |
| USB | Micro USB 5Pin, High speed USB 2.0 |
| Power Supply | DC IN | DC 5 / 1.2A |
|  | Built-in Li-Ion battery | 3.7V/ 500mAh |
| Dimensions | 65(L)X37(W)X20(H)mm (Not include prominent part) |
| Weight | g |
| Operating Temperature | 0℃～+50℃ |

System Content

SKY-HD01                 5.8G 2dBi antenna X 1              7-30V to 5V Power Board

Micro 5Pin USB Cable        4Pin OSD Cable      5V USB Power cable   3P TX Remote control cable