Model#:  	HB25T

Product Name:    	Power Switchable Micro Camera

Introduction:

This micro 600TVL CMOS camera integrated 5.8GHz 40CH video transmitter (power switchable) all together provides super compact and ultra-light vision solution for any size FPV vehicle.

Specifications:

- Electrical:

  - Power Supply:	DC 4.8-24V

  - Current:	150mAh @12V (200mW) / 90mAh @ 12V (25mW)

  - Power Switchable:	25mW / 200mW (by push button)

  - Format:	NTSC / PAL

  - Port:	3p JST connector (GND, Power, PWM signal)

  - Channel Display:	Digital Tube

  - Channel Selection:	Push Button / PWM

  - Antenna gain:	3db

  - Frequencies:

| Band\Channel | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Band A | 5705MHz | 5685MHz | 5665MHz | 5645MHz | 5885MHz | 5905MHz | 5925MHz | 5945MHz |
| Band B | 5733MHz | 5752MHz | 5771MHz | 5790MHz | 5809MHz | 5828MHz | 5847MHz | 5866MHz |
| Band C | 5725MHz | 5745MHz | 5765MHz | 5785MHz | 5805MHz | 5825MHz | 5845MHz | 5865MHz |
| Band D | 5740MHz | 5760MHz | 5780MHz | 5800MHz | 5820MHz | 5840MHz | 5860MHz | 5880MHz |
| Band E (RaceBand) | 5658MHz | 5695MHz | 5732MHz | 5769MHz | 5806MHz | 5843MHz | 5880MHz | 5917MHz |

  - PWM function:

| Channel | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PWM | 1150μs | 1250μs | 1350μs | 1450μs | 1650μs | 1750μs | 1850μs | 1950μs |

Note: when PWM detected at 1500μs then auto transfer to button control mode.

- Optical:

  - FOV:	120°

  - Imager:	1/4” 600TVL CMOS

  - Format:	NTSC or PAL

- Audio:

  - Microphone:	Available

- Mechanical:

  - Dimension: 	23*19*22mm

  - Antenna Size:	25*14mm

  - Transmitter Weight: 	7 g

  - Accessories: 	1 x 3pin JST silicone cable

- Operation:

  - Button1: Power Control

- When power is on, short press Button1 twice to start transmission and LED 5 will turn on; and short press Button1 twice to stop transmission.

- Long press Button1 for 5s, Dot 6 is on to indicate 200mW and off to indicate 25mW.

- Auto save last time transmission setting: if transmission set as on / off before power off, then next time when power on, it will remain last time transmission setting as on / off.

  - Button2: Band/Channel Control

- Long press Button2 for 3s to change Band from A to E.

- Short press Button2 to change Channel from 1 to 8.

- Digital Tube will display Band/Channel.

  - Position 3: PAL/NTSC Selection

  - Solder Pin3 and Pin4 together as NTSC, Unsolder Pin3 and Pin4 as PAL.

  - Position 4: OSD Selection

  - Pin3 and Pin4 default as connected (video signal directly passing from camera to Tx).

  - Camera video output from Pin3, Tx input from Pin4.

  - If OSD is intended, unsolder Pin3 and Pin4; Connect Pin4 for OSD input and connect Pin3 for OSD output.