目前主流的F3飞控，缩小版的Omnibus F3, 集成Betaflight OSD自带Betaflight在线配置OSD界面，采用MPU6000传感器并通过SPI总线连接，提高传感器的采样速率，提高MCU主控程序的运行频率，提供更高的控制精度和更快的响应速度。兼容60MM-80MM小型无刷四轴机架。

接收机的配置，SBUS和DSM接收机输入时，请配置RX3(UART3)为输入接口。

DSM/DSM2/DSMX接收机从3.3V取电。

SBUS和PPM接收机从5V取电。

出厂固件：betaflight_3.1.0_OMNIBUS

最新的固件支持Dshot协议电调

特点：

CPU:  STM32F303CCT6  (72MHZ, 256K FLASH)

传感器： MPU-6000 三轴加速度计/三轴陀螺仪 (SPI连接)

供电： 2S 电池输入

BEC： 内置5V/0.5A

接收机：PPM，支持Sbus或串口RX接口,Spektrum 1024/2048, SBUS, XBUS, SumD 和 SumH RX内置反向器

支持 3.3V Spektrum 卫星接收机

蜂鸣器接口

支持可编程LED Sprit（使用前关掉Transponder）

支持 BLheli suite Pass-through电调编程

内置电压检测、报警

板子尺寸：20*20MM

螺丝孔间距: 16*16MM  直径2.0MM

板子重量：1.9克

Specification:
Item name: Super_s F3 flight controller board
Size: 20*20mm
Mounting hole: 16*16mm
Diameter: 2mm
Weight: 1.9g
Processor: STM32F303CCT6 (72MHZ, 256K FLASH)
Sensor: MPU-6000 ( connected by SPI)
Firmware version: betaflight_3.1.0_OMNIBUS
Built-in ESC: 5V/0.5A
Receiver: PPM, Spektrum 1024/2048, SBUS, IBUS, XBUS, SumD SumH RX etc.
Power supply: 2S lipo battery ( 6.5V-8.4V)
Suitable for 60mm-80mm mini brushless FPV Quadcopter frame

Features:
-Support programmable LED Sprit (turn off transponder before using)
-Support BLheli/BLHELI_S suite Pass-through ready
-Support PPM, Oneshot125, Oneshot42, Multishot, Dshot150, Dshot300, Dshot600
-Support the newest DSHOT ESC
-Built-in voltage detection, alarm
-Built-in Betaflight-OSD
-Buzzer solder pin
-LED_STRIP connector
-BB ring

Package included:
1* flight control board

Notes:
-DSM and SBUS receiver input, please configure RX3(UART3) as input interface.
-DSM receiver power from 3.3V.
-SBUS and PPM receiver power from 5V.