中文名称Super_S BS06D 4合1 6A Blheli_S 2S电调 DSHOT 16mmx16mm

英文名称 Super_S BS06D 4in1 6A Blheli_S 2S ESC Dshot600 ready 16mmx16mm

Description:
Item name: Super_s 4 In 1 6A BLHeli_S ESC
Size: 25x29mm (includes solder pad)
Mounting holes: 16x16mm, φ2mm
Weight: 3g
Input voltage: 2S lipo
Con. Current: 6A
Peak Current: 10A (5S)
Firmware: BLHELI_S
Processor: SILABS EFM8BB21F16G
BEC: NO
Driver: 3 in 1 MOS
Supports Dshot Oneshot multishot

Package include:
1 x Super_S 4 In 1 6A BLHeli_S ESC
1 x Cable

4 x M2*5+5 nylon columnd

4 x M2 Screw

4 x M2 Nut

技术参数：
1.输入电压:2S LiPo
2.BEC输出:无
3.单个电调持续工作电流:6A （最大电流:10A 5秒）
4.四合一电调尺寸:25*29mm（包含焊盘及突出点最大尺寸）螺丝孔尺寸2mm

安装孔距16*16MM
5.四合一电调重量:2.7g
6.固件: BLHELI_S
7.支持DSHOT150/300/600，Oneshot，multishot 
8.处理器：SILABS  EFM8BB21F16G

9.适合Racewhoop, Super_S F3, Super_S F4飞控组件超小型飞塔

发货包装包括：

Super_s BS06D 4合1 电调 x1

6pin 连接线 x1

M2尼龙柱 x4

M2 螺丝 x4

M2 螺母x4

BLHELISUITE电调调试软件下载地址

https://www.mediafire.com/folder/dx6kfaasyo24l/BLHeliSuite